## Slide 1
CROWD ANOMALY CUEING
Designed around the swarm-analytics patent, by construction
The prior-art claim tracks device locations and auto-notifies responders. Our flow uses aggregate RAN telemetry, keeps a human in the loop, and acts first as coverage optimization.
PRIOR-ART PATENT (US 10,032,361, swarm analytics)
OUR APPROACH (Crowd Anomaly Cueing)
1. Ingest collective real-time device location data
✓ Ingest aggregate RAN beam telemetry only: per-beam UE counts, centroid, spread. No device location tracking.
2. Detect movement of the group away from a central point
✓ Detect an abnormal change in the count distribution across beams (spread rising, centroid velocity). A shape change, not device motion from a point.
3. Classify the pattern as a threat condition
✓ Do not classify as a threat. Flag an anomaly only. The network sees an effect, never claims a cause.
4. Automatically notify a first responder
✓ Raise an advisory flag to the network operator, and cue a camera. Human verifies. Never auto-notifies a responder, never auto-dispatches.
(no equivalent step)
+ Primary action is coverage assurance: widen or re-steer beams (O-RAN A1/O1 intent) to keep the dispersing crowd connected. A network-optimization action, outside the patent's scope entirely.
For legal review: confirm the input is aggregate RAN telemetry, not device-location data; confirm actuation is operator-advisory plus coverage optimization, never auto-notification of a responder. Not an FTO opinion, run the actual claims past Nokia IP before build or external pitch.